## Slide 1: Range-Rate OD
2021-07-04

## Slide 2: Assumptions
Know range-rate to >= 3 pulsars at >= 3 known times each
Know gravitational parameter () of central body
Know pulsar coordinates in inertial frame (e.g., SSB)

## Slide 3: Hodograph Review
x
y

## Slide 4: Approach – Guess f0, e, dM
Mean anomaly span (dM)
  Get orbit period using ToF
  Get semi-major axis using
Eccentricity (e)
  Get hodograph radius
Initial true anomaly (f0)
  Get true anomaly of each measurement
Search solution space using multi-start + fminsearch

## Slide 5: Objective Function 1: Sinusoid Fit
Range-rate vs. true anomaly plot is a sinusoid:
  = right ascension, referenced to
  = declination
Can solve for , using linear least squares:
*for pulsar k

## Slide 6: Objective Function 2: Pulsar Alignment
Know angle between pulsars
Know angle between derived pulsars (calculated from and )
Can calculate error in dot product between each pair of pulsars, and sum the error for each pair

## Slide 7: Objective Function 3: Frame Alignment
Find coordinate system using sinusoid and true pulsars
  Full velocity vectors can be found using sinusoids at the same true anomaly
Find and for true pulsars in this coordinate system
Compare against and values found from the sinusoid fit

## Slide 8: Objective Function Summary

## Slide 9: Algorithm
Search for minimum objective function in 35 x 35 x 35 grid of evenly spaced points
Use fminsearch to find solution
  fminsearch uses the Nelder-Mead algorithm
Original Grid
Shifted Along Y
Shifted Along X

## Slide 10: Limitations
Slow compared to analytic OD methods
  6-10 seconds per run, depending on number of measurements & grid size
Certain orbits need finer search
  Some orbits only need 25^3, while others need 35^3
  Unclear which orbits. Heuristically:
    Eccentricity near 0 or 1
    Mean anomaly span near 0
Currently only for elliptic orbits + measurements within 1 orbit period
  Work in progress – should be easy to fix these
Proof that global min exists and is near true solution?

## Slide 11: Noise Model
To fairly compare RROD and VIOD, we do the following:
  At , take range-rate to pulsars , then repeat at
  i.e. the full velocity vector may be assembled
Adding noise:
  Perturb each range-rate measurement with normally distributed noise
    Zero mean, uncorrelated
  Fully velocity vector is assembled from perturbed range-rate data
    Intersection of three or more planes

## Slide 12: Preliminary Results
410 km LEO (similar to StarNav ex.), e = 0.03, f0 = 10 deg,
dT = 90 mins (92%), noise = 0.5m/s, #obsv = 90, #sim = 200
Not an exact replica of StarNAV:
Simpler noise model
StarNAV-VIOD had some issues with e = 0 / f0 = 0
StarNAV-VIOD better than pure VIOD
Consistent with StarNAV results
Need more quantitative comparisons
RROD significantly better than both – why?
Does the noise model give RROD an unfair advantage?

## Slide 13: Preliminary Results
Earth-Mars Hohmann transfer, e = 0.21, f0 = 140 deg
dT = 10.3 days (2%), noise = 0.5m/s, #obsv = 10, #sim = 300
RROD is 25 times more accurate than VIOD
StarNAV-VIOD does not perform better than regular VIOD in this case
Neptune case not shown – RROD is about two orders of magnitude better

## Slide 14: Using Imaginary Pulsars
What if we create range-rate data from velocity vectors?
Fairest possible comparison – RROD has no accesses to additional data
RROD_Im method pretends that the x-, y-, and z-axis values of the velocity vector used for VIOD are its range-rate measurements
RROD_Im still performs better than VIOD!
Earth-Mars Hohmann transfer, e = 0.21, f0 = 90 deg
dT = 25 days (5%), noise = 0.5m/s, #obsv = 20, #sim = 100

## Slide 15: Using Imaginary Pulsars
The “imaginary pulsar” method does not always do well – several outliers exist in this case
Need more testing to figure out when this method fails
410 km LEO, e = 0.03, f0 = 10 deg
dT = 90 mins (92%), noise = 0.5m/s, #obsv = 50, #sim = 70

## Slide 16: Considerations
How to benchmark this method? Many variables
  All VIOD variables
  Number of pulsars
  Arrangement of measurements (timing, order)
Improving the noise model
  Look for existing range-rate noise models

## Slide 17: Summary
Developed relations between range-rate and the hodograph
Developed objective function and algorithm to perform RROD
Range-rate OD appears to be feasible
Method seems capable of outperforming VIOD