## Slide 1: Range-Rate OD
2021-07-04

## Slide 2: Assumptions
Know range-rate to >= 3 pulsars at different times
Know gravitational parameter () of central body
Know pulsar coordinates
Know time of flight (ToF) between range-rate measurements

## Slide 3: Approach – Guess f0, e, dM
Mean anomaly span (dM)
  Get orbit period using ToF
  Get semi-major axis using
Eccentricity (e)
  Get hodograph radius
Initial true anomaly (f0)
  Get true anomaly of each measurement
Search solution space using multi-start + fminsearch

## Slide 4: Objective Function 1: Sinusoid Fit
Range-rate vs. true anomaly plot is a sinusoid:
  = pulsar inclination relative to orbit plane
  = pulsar rotation about , starting from
Can solve for , using linear least squares:
*for pulsar k

## Slide 5: Objective Function 2: Pulsar Alignment
Know angle between pulsars
Know angle between derived pulsars (calculated from and )
Can calculate error in dot product between each pair of pulsars, and sum the error for each pair

## Slide 6: Objective Function 3: Frame Alignment
Find coordinate system using sinusoid and true pulsars
  Full velocity vectors can be found using sinusoids at the same true anomaly
Find and for true pulsars in this coordinate system
Compare against and values found from the sinusoid fit

## Slide 7: Objective Function Summary

## Slide 8: Algorithm
Search for minimum objective function in 50 x 50 x 50 grid of evenly spaced points
Use fminsearch to find solution
  Nelder-Mead algorithm
Original Grid
Shifted Along Y
Shifted Along X

## Slide 9: Limitations
Slow compared to analytic OD methods
  6-10 seconds per run, depending on number of measurements
Extreme values need finer search
  Eccentricity near 0 or 1
  Mean anomaly span near 0
Elliptic orbits, measurements within 1 orbit period
  Work in progress – should be easy to fix these
Proof that global min exists and is near true solution?

## Slide 10: Noise Model
To fairly compare RROD and VIOD, we do the following:
  At , take measurements from pulsars , then repeat at
  i.e. the full velocity vector may be assembled
Adding noise:
  Perturb each range-rate measurement with normally distributed noise
    Zero mean, uncorrelated
  Fully velocity vector is assembled from perturbed range-rate data
    Intersection of three or more planes

## Slide 11: Preliminary Results
410 km LEO (similar to StarNav ex.), e = 0.03, f0 = 10 deg,
dT = 90 mins (92%), noise = 0.5m/s, #obsv = 90, #sim = 200
Not an exact replica of StarNAV:
Simpler noise model
StarNAV-VIOD had some issues with e = 0 / f0 = 0
StarNAV-VIOD better than pure VIOD
Consistent with StarNAV results
Need more quantitative comparisons
RROD significantly better than both – why?
Does the noise model give RROD an unfair advantage?

## Slide 12: Preliminary Results
Earth-Mars Hohmann transfer, e = 0.21, f0 = 140 deg
dT = 10.3 days (2%), noise = 0.5m/s, #obsv = 10, #sim = 300
RROD is 25 times more accurate than VIOD
StarNAV-VIOD does not improve better than regular VIOD in this case
Neptune case not shown – RROD is about two orders of magnitude better

## Slide 13: Considerations
How to benchmark this method? Many variables
  All VIOD variables
  Number of pulsars
  Arrangement of measurements (timing, order)