## Slide 1: Range-Rate OD
2021-07-04

## Slide 2: Assumptions
Know range-rate to >= 3 pulsars at different times
Know pulsar coordinates
Know time elapsed between range-rate measurements

## Slide 3: Approach – Guess f0, e, dM
Mean anomaly span (dM)
  Get orbit period
  Get semi-major axis
Eccentricity (e)
  Get hodograph radius
Initial true anomaly (f0)
  Get true anomaly of each measurement
Search solution space using brute force + gradient descent

## Slide 4: Objective Function 1: Circle Fit
Range-rate vs. true anomaly plot is a sine wave:
  = pulsar inclination relative to orbit plane
  = pulsar rotation about , starting from
Can solve for , using linear least squares:
*for pulsar a

## Slide 5: Objective Function 2: Pulsar Alignment
Know angle between pulsars
Know angle between derived pulsars (calculated from and )
Can calculate angle between each pair of pulsars, and sum the error for each pair

## Slide 6: Objective Function 3: Frame Alignment
Find coordinate system using sine wave and true pulsars
  Full velocity vectors can be found using sine waves at the same true anomaly
Find and for true pulsars in this coordinate system
Compare against and values found from the circle fit

## Slide 7: Algorithm
Brute force search solution space (10 x 10 x 10 usually sufficient), apply fminsearch for each guess
fsolve
Reduce search radius, re-center at best solution
Repeat steps 1-3 until objective function converges

## Slide 8: Limitations
Slow compared to analytic OD methods
  5-20 seconds per run, depending on resolution of brute force search
Extreme values need finer search
  Eccentricity near 0 or 1
  Mean anomaly span near 0
Elliptic orbits, measurements within 1 orbit period
  Work in progress – should be easy to fix these
Proof that global min exists and is near true solution?

## Slide 9: Temp
Text

## Slide 10: Considerations
How to benchmark this method? Many variables
  All VIOD variables
  Number of pulsars
  Arrangement of measurements (timing, order)